## Slide 1
  Flotation Requirements for Recreational Boats

## Slide 2: FLOTATION
Flotation requirements can be found in
TITLE 33 CFR SUBPART F, G, H Beginning with 33 CFR 183.101
ABYC H-8 BUOYANCY IN THE EVENT OF SWAMPING

## Slide 3: FLOTATION
Applies To:
MONOHULL RECREATIONAL BOATS
UNDER 20 FEET
DOES NOT INCLUDE CANOES KAYAKS INFLATABLES MULTIHULLS SUBMERSIBLES RACEBOATS SURFACE EFFECT AMPHIBIOUS VEHICLES VEHICLES SAILBOATS

## Slide 4: FLOTATION
For the following see ABYC Standards
CANOES & KAYAKS SEE H-29
INFLATABLE BOATS SEE H-28
PONTOON BOATS SEE H-35

## Slide 5: FLOTATION
TYPES OF FLOTATION
  BASIC (33 CFR 183.101)
  LEVEL (33 CFR 183.201)
  MODIFIED LEVEL (33 CFR 183.301)

## Slide 6: BASIC FLOTATION
MONOHULLS UNDER 20 FEET
INBOARDS
STERNDRIVES
AIRBOATS
JETBOATS
APPLICATION (33 CFR 183.101)

## Slide 7: BASIC FLOTATION
Exception
Mini Jet Boats must meet:
FED REGS – Basic (33 CFR 183.101)
Or:
ABYC H-8, 8.5.1 – Level Flotation

## Slide 8: BASIC FLOTATION -
Photo Courtesy U.S.Marine
Example: a typical stern drive boat

## Slide 9: BASIC FLOTATION
BASIC FLOTATION REQUIREMENTS
AFTER 18 HR SOAK WITH THE BOAT SWAMPED: SOME PORTION OF THE BOAT MUST BE OUT OF THE WATER WITH WEIGHTS FOR:
  2/15 OF PERSONS CAPACITY.
  25% OF DEAD WEIGHT.
    DEAD WEIGHT = MAX WT - PERSONS WT
  62.4 LB TIMES VOLUME OF THE TWO LARGEST AIR CHAMBERS, IF USED.

## Slide 10: BASIC FLOTATION
BASIC FLOTATION REQUIREMENTS
  AIR CHAMBERS INTEGRAL WITH THE HULL NOT ALLOWED. (33 CFR 183.112(b))
  IF AIR CHAMBERS ARE USED; THE 2 LARGEST WILL BE PUNCTURED DURING THE TEST.

## Slide 11: BASIC FLOTATION
  NOTE: ABYC H-8.7.3.1.2, SAYS THAT IN ADDITION TO THE ABOVE: “WEIGHTS THAT, WHEN SUBMERGED, EQUALS 75% OF THE DRY WEIGHTS OF THE PROPULSION SYSTEM AND BATTERY(S).”
  ABYC Assumes you will test without the engines and sterndrive installed.
  The Coast Guard tests the boat with the engines installed but removes the sterndrive and batteries and substitutes weights.
Engines

## Slide 12: LEVEL FLOTATION
OUTBOARDS UNDER 20 FEET OVER 2 HP
APPLICATION
Photo Courtesy of U. S. Marine

## Slide 13: LEVEL FLOTATION - Tests
AFTER 18 HR SOAK
  SUPPORT 275 LBS + .125 X (PERSONS WT - 550 LB.)
  SUPPORT 25% OF DEAD WT
    DEAD WEIGHT = MAX WT MINUS- TABLE 4
    COL 6 WEIGHT FOR THE ASSIGNED.
    HORSEPOWER – MINUS PERSONS CAPACITY.
    If DEAD WEIGHT IS LESS THAN ZERO
    (NEGATIVE) THEN IT EQUALS ZERO.

## Slide 14: LEVEL FLOTATION Weights
Placement of Weights
CG OF WEIGHTS IS IN THE 40% REFERENCE AREA
WEIGHTS FOR MOTORS, CONTROLS AND BATTERIES PLACED IN THE NORMAL OPERATING POSITION
FUEL TANKS: REGULATION SAYS FUEL TANKS MUST BE FULL AND SEALED. HOWEVER, NOT A GOOD IDEA. USE WEIGHTS TO SIMULATE THE TANK WEIGHT OR FILL TANK ¾ FULL WITH WATER.

## Slide 15: REFERENCE AREAS

## Slide 16: REFERENCE AREAS

## Slide 17: Measuring Reference Areas

## Slide 18: Measuring Reference Areas

## Slide 19: LEVEL FLOTATION - Results
  NOT MORE THAN 10 DEGREE HEEL
  FORWARD OR AFT REFERENCE AREA OUT OF THE WATER
  REFERENCE AREA NOT MORE THAN 6” UNDER WATER
  SUPPORTS 62.4 TIMES VOLUME OF THE TWO LARGEST AIR CHAMBERS, IF USED

## Slide 20: FLOTATION TEST RESULTS

## Slide 21: FLOTATION TEST RESULTS

## Slide 22: LEVEL FLOTATION Stability
STABILITY PORT AND STARBOARD
  SUPPORT ½ OF (275 LBS + .125 X (PERSONS WEIGHT - 550 LB.))
  SUPPORT 25% OF DEAD WEIGHT
  C. G. OF PERSONS WEIGHT PLACED IN 70% REFERENCE AREA SO THAT CG IS 4 IN. ABOVE FLOOR OR 4 INCH ABOVE SEAT.
  WEIGHTS FOR MOTORS CONTROLS AND BATTERIES PLACED IN THE NORMAL OPERATING POSITION

## Slide 23: LEVEL FLOTATION- Results
  NOT MORE THAN 30 DEG HEEL
  FORWARD OR AFT REFERENCE AREA OUT OF WATER
  REFERENCE AREA NOT MORE THAN 12” UNDER WATER

## Slide 24: LEVEL FLOTATION -Test

## Slide 25: LEVEL FLOTATION -Test

## Slide 26: FLOTATION TEST - Results

## Slide 27: LEVEL FLOTATION - Test
TEST WITHOUT PERSONS WEIGHT
  REMOVE PERSONS WEIGHT
  NOT MORE THAN 10 DEGREE HEEL
  FORWARD OR AFT REFERENCE AREA OUT OF WATER
  SUBMERGED REFERENCE AREA NOT MORE THAN 6” UNDER WATER

## Slide 28: LEVEL FLOTATION -Test

## Slide 29: MODIFIED LEVEL FLOTATION
OUTBOARDS 2 HP OR LESS and:
MANUALLY PROPELLED BOATS
  INTEGRAL AIR TANKS ARE ALLOWED
  NO AIR TANKS ARE PUNCTURED
APPLICATION – 33 CFR 183.301

## Slide 30: MODIFIED LEVEL FLOTATION
Photo Courtesy of Walker Bay

## Slide 31: MODIFIED LEVEL FLOTATION
REQUIREMENTS
  AFTER 18 HOUR SOAK
  SUPPORT 2/15 PERSONS WT + 25% ( MAX WT - COL 6 TABLE 4 WT - PERSONS WT)

## Slide 32: MODIFIED LEVEL FLOTATION
Placement of Weights
CG OF WEIGHTS IS IN THE 40% REFERENCE AREA
WEIGHTS FOR MOTORS, CONTROLS AND BATTERIES PLACED IN THE NORMAL OPERATING POSITION

## Slide 33: MODIFIED LEVEL FLOTATION
  RESULTS
  NOT MORE THAN 10 DEGREE HEEL
  FORWARD OR AFT REFERENCE AREA OUT OF WATER
  SUBMERGED REFERENCE AREA NOT MORE THAN 6” UNDER WATER

## Slide 34: MODIFIED LEVEL FLOTATION
STABILITY PORT AND STARBOARD
  REMOVE 1/2 OF AMOUNT TO SIMULATE PERSONS
  PLACE 1/2 PERSONS WT IN 70% AREA
  LEAVE WTS FOR ENGINE & BATTERY

## Slide 35: MODIFIED LEVEL FLOTATION
  NOT MORE THAN 30 DEGREE HEEL
  FORWARD OR AFT REFERENCE AREA OUT OF THE WATER
  SUBMERGED REFERENCE AREA NOT MORE THAN 12” UNDER WATER

## Slide 36: MODIFIED LEVEL FLOTATION
TEST WITHOUT PERSONS WEIGHT
  REMOVE PERSONS WEIGHT FROM BOAT
  LEAVE WTS FOR ENGINE & BATTERY
  NOT MORE THAN 10 DEGREE HEEL
  FORWARD OR AFT REFERENCE AREA OUT OF WATER
  SUBMERGED REFERENCE AREA NOT MORE THAN 6” UNDER WATER

## Slide 37: FLOTATION MATERIALS
FOAM USED IN THE FOLLOWING PLACES MUST MEET
THE PRESCRIBED TESTS:
VAPOR TEST --------------------------- X 24 HR GAS ------ X 30 DAY GAS ---------------------------------------------- X 24 HR OIL ------ X 30 DAY OIL ---------------------------------------------- X 24 HR BILGE ------ X CLEANER 30 DAY BILGE -------------------------------------------- X CLEANER
Engine Room Engine Room Bilge
Unless Open to Atmosphere

## Slide 38: FLOTATION MATERIALS
FLOTATION FOAM DOES NOT
REQUIRE CG APPROVAL
This means that there is no process by which the Coast Guard tests and approves foam for flotation. A foam vendor claiming their foam is Coast Guard Approved is misinformed.
Any means the manufacturer of the boat wants to use to meet
the performance requirements is allowed.

## Slide 39: FLOTATION MATERIALS
Milk Bottles - clever –but not recommended. Boat failed due to metal caps on the bottles. Caps rusted and leaked water into the bottles. Had they used plastic sealed caps it might have passed

## Slide 40: FLOTATION MATERIALS
Two pound density closed cell foam. Recommended! A good example.

## Slide 41: TABLE 4; 33 CFR Subpart H
Table 4--Weights (Pounds) of Outboard Motor and Related Equipment for Various Boat Horsepower Ratings
____________________________________________________________________________________
Boat horsepower rating Motor and control weight Battery weight Full portable fuel tank 1+3+5
Dry Swamped Dry Submerged weight
____________________________________________________________________________________
Column No.
____________________________________________________________________________________
1 2 3 4 5 6
____________________________________________________________________________________
0.1 to 2 25 20 25
2.1 to 3.9 40 34 40
4.0 to 7 60 52 25 35
7.1 to 15 90 82 20 11 50 160
15.1 to 25 125 105 45 25 50 220
25.1 to 45 170 143 45 25 100 315
45.1 to 60 235 195 45 25 100 380
60.1 to 80 280 235 45 25 100 425
80.1 to 145 405 352 45 25 100 550
145.1 to 275 430 380 45 25 100 575
275.1 and up 605 538 45 25 100 750
____________________________________________________________________________________
Transoms designed for twin motors
____________________________________________________________________________________
50.1 to 90 340 286 90 50 100 530
90.1 to 120 470 390 90 50 100 660
120.1 to 160 560 470 90 50 100 750
160.1 to 290 810 704 90 50 100 1000
290.1 to 550 860 760 90 50 100 1050
550.1 and up 1210 1076 90 50 100 1400
____________________________________________________________________________________

## Slide 42: ABYC S-30 OUTBOARD ENGINE AND RELATED EQUIPMENT WEIGHTS

## Slide 43: FLOTATION Calculations
Determining the amount of flotation needed:
Wh = Dry weight of hull below swamped waterline
Wd = Dry weight of deck and superstructure
We = Dry weight of factory installed equipment
hardware and accessories.
K1 & K2 = conversion factors for material from Table I in ABYC H-8
B = Buoyancy of flotation material in pounds per cubic foot.
G = Weight of Machinery (engines, sterndrives, outboards, etc.)
NMMA
Certification
Handbook
Uses the Same Notation and Formulas

## Slide 44: CONVERSION - Calculations

## Slide 45: FLOTATION Calculations
Determine the amount of Flotation to Support the following
Fb = Amount of Flotation need to support the swamped boat
Fp = Flotation needed to support propulsion equipment
Fc = Flotation needed to support persons and dead weight

## Slide 46: BASIC FLOTATION EXAMPLE Boat Weight
See H-8 Page 3 8.7.2.1.1
Fb = Amount of Flotation need to support the swamped boat
Fb = (Wh x K1) + (Wd x K2) + (0.69 We) / B
B = 62.4 For Air Chambers
B = 60.4 For 2 pound density foam.

## Slide 47: BASIC FLOTATION EXAMPLE
BASIC FLOTATION EXAMPLE
Wh = 600 pounds (Fiberglass)
Wd = 120 pounds (Plywood)
We = 50 pounds (Equipment hardware and Access.)
K = Factor for each type of material to find submerged wt. (see Table 1 H-8)
Fb = ((Wh x K1) + (Wd xK2) + (0.69 x We) / B
Fb = ((600x0.33)+(120x -0.81)+(0.69x50)/ 60.4
Fb = (198 - 97.2 + 34.5) / 60.4
Fb = 135.3 /60.4
Fb = 2.24 Cubic Feet 2 Lb Density Foam

## Slide 48: BASIC FLOTATION EXAMPLE
Engine
Weight of Propulsion System including sterndrive and battery = 900 LB
Fp = Flotation needed to support propulsion equipment
Fp = G / B
G = 0.75 x installed weight of sterndrives & inboards
Example: Fp = G/B = (900 x.75) /60.4 = 675/60.4
Fp = 11.18 Cubic Feet 2 lb density foam

## Slide 49: BASIC FLOTATION EXAMPLE - Persons
Flotation needed to support persons and dead weight.
Maximum Weight Capacity = 2400 lb.
Fuel tank = 40 gals = 240 lbs.
Fc = .25(Fc1 + Fc2) /B
Fc1 = Maximum Persons Capacity – Fuel Wt. = 2160 lb.
Fc2 = Maximum Weight Capacity - Maximum Persons Capacity
Fc = 0.25 (Fc1 + Fc2) /B = .25((2400-240) + (2400 - 2400) / 60.4
Fc = 540 / 60.4 = 8.94 Cubic feet 2 lb density foam

## Slide 50: BASIC FLOTATION EXAMPLE
Basic Flotation Sample
Total Flotation Requirements:
F = Fb + Fp + Fc
2.24 Cu Ft - Round to 2.3 - To float hull and deck
11.18 Cu Ft - Round to 11.2 - to support engine
8.94 Cu Ft - Round to 9 - to support people & dead wt
22.36 Cu Ft. Round to 22.5 Cu Ft.
Total 22.5 Cu Ft

## Slide 51: LEVEL FLOTATION Example
See H-8 page 5, 8.8.2
Outboard Powered boat
HP = 140
Maximum Weight Capacity = 1600 LB
Maximum Persons Capacity = 887 LB

## Slide 52: LEVEL FLOTATION Example Boat Weight
Wh = Dry Weight of Hull Material
Whf = Weight of Fiberglass Hull = 500 Lb
Whp = Weight of Plywood in Hull = 220 Lb
Wd = Weight of deck & equipment = 185 lb
K = Factor for each type of material to find submerged weight
Fb = Flotation to float the swamped boat
Fb = ((Wh x K) + Wd) / B
Wh x K = (Whf x Kf) + (Whp x Kp)
Fb = ((500x 0.33) + (220 x -0.81) + (185)) / 60.4
Fb = (165-178.2+185) / 60.4
Fb = 171.8 / 60.4 = 2.85 Cu Ft. of 2 lb density foam

## Slide 53: Level Flotation Sample - Engine
Calculation for flotation to support swamped engine.
HP = 140
G = swamped weight from ABYC S-30 Table 1a Col. 4, for outboards = 453 Pounds
Submerged Battery Weight = 25 LB (S-30 Table 1a, Col. 8)

## Slide 54: Level Flotation Sample - Engine
Fp = G/B
Fp = 453 + 25 / 60.4
Fp = 478 / 60.4
Fp = 7.91 Cu. Ft. 2 lb density foam

## Slide 55: Level Flotation Sample Persons Capacity
Calculation for flotation needed to support persons capacity and deadweight.
Maximum Weight Capacity = 1600 lb. 140 HP Outboard (From table S-30 Col 10) = 713 lb.
Persons Capacity = 887 lb.
Fc = 1/2 (550 lb) + 1/12 (Persons Capacity - 550) + .25 (Dead Weight)/60.4
Fc = 1/2 first 550 lbs + 1/12 (887-550) + .25 (deadweight)/60.4
Fc = (0.5(550) + 0.125(887-550) + (0.25(1600-713-887))/60.4
Fc = 275 +42.125 + 0) / 60.4
Fc = 317.125 /60.4 = 5.25 Cu Ft

## Slide 56: Level Flotation Sample
Total Flotation Requirement
2.85 Cu Ft - round to 3.0 - to float deck & hull
7.91 Cu Ft - round to 6.3 - to float engine & equipment
5.25 Cu Ft - round to 5.6 - to float persons and deadweight
Total 16.01 Cu Ft.
All of the preceding examples were taken directly from ABYC H-8 and the engine weights were taken from Table 1a in S-30.

## Slide 57: FLOTATION LOCATION
Where Do you put the flotation?
Location
Location
Location

## Slide 58: FLOTATION LOCATION

## Slide 59: FLOTATION LOCATION

## Slide 60: FLOTATION LOCATION

## Slide 61: FLOTATION LOCATION

## Slide 62: FLOTATION LOCATION

## Slide 63: FLOTATION LOCATION

## Slide 64: Test Procedures - Issues
Permanently Installed Fuel Tanks:
20 Gals or Less. Place weight of fuel on deck over CG of Fuel Tanks.
Greater Than 20 Gal.: Initially same as above. If boat fails fill tank to ¾ level with water. If still fails fill tank full with water.
Time Allowed to stabilize between tests: 15 minutes.
Hull to Deck Joint:
Seal Hull to deck Joint with tape on all boats prior to test.

## Slide 65: Test Procedures
Location Of Outboard Motor Weight
3 Inches aft of transom. (+/- 1 inch)
3 inches above transom. (+/- 1 inch)
Flooded Bait Wells During Flotation Tests
Remove riser from drain hole and let bait well flood /drain naturally.
Trolling Motor Weight for Flotation Test.
If equipped with or wired for a trolling motor, the trolling motor and battery are to be considered gear weight.

## Slide 66: Test Procedures
Kicker Motors:
If the boat is equipped with a pad or wiring for a kicker motor then flotation must be provide for the submerged weight of motor and controls.
If the manufacture of the boat does not specify the horsepower for the kicker motor the the horsepower will be assumed to be 10% of the main motor’s horsepower. Weights will be from table 4 .

## Slide 67: FLOTATION FAILURES
Marginal Failures.
Current and future production (no recall) if the amount of foam missing is less than or equal to:
FT cubed = Boat Length X 0.025
IF GREATER THAN THE ABOVE AMOUNT THE MANUFACTURER MUST DO A RECALL.

## Slide 68: FLOTATION PROBLEMS
    Use heaviest production tolerances; o/b boats grow in weight
    Watch out for too much flotation
    Be careful of the placement of flotation:
      Typically too much in the bottom
      Too high (out of the water)
      Too low
Beware of changes in a model without looking at the amount of flotation.

## Slide 69: FLOTATION PROBLEMS
    Foam Problems
      Water soaked foams
      Foams that don’t foam properly
        Too hot
        Too cold
        Humidity
        Dirty &/or un-calibrated guns
        Wrong ratios (two part foams)
Follow the foam Manufacturers Instructions

## Slide 70: FLOTATION The Good, The Bad, the Ugly

## Slide 71: FLOTATION The Good, The Bad, the Ugly

## Slide 72: FLOTATION The Good , The Bad, The Ugly
TOO COLD!

## Slide 73: FLOTATION The Good , The Bad, The Ugly
TOO
HOT!

## Slide 74: FLOTATION
    TYPICAL PROBLEMS
    Do a Test
    USE BLOCK FOAM
    RECALLS: How do you fix the problem. More foam? Or less capacity? Change label or add foam?

## Slide 75: Level Flotation Demo
Photo courtesy Walker Bay

## Slide 76: Level Flotation Demo
Boat Capacities

## Slide 77: Level Flotation Demo
Maximum Persons Weight = 360
Maximum Weight Capacity = 425
Maximum Horsepower = 2
Engine Weight From ABYC S-30 = 30 lb.

## Slide 78: Level Flotation Demo
Calculations For Level Flotation Tests
2/15 of the Persons Capacity = 2/15 of 360 = 48 lb
Engine and fuel tank weight = 30 lb
25% of gear weight = Max Wt Cap – Max Pers Wt – motor weight = .25 (425-360-30) = 8.75 lb
Swamped Motor weight From S-30 = 26 lb
Total Weight needed = 48 + 8.75 + 26 = 82.75 lb

## Slide 79: Level Flotation Demo
Weight of Submerged Weights
Weights do not weigh the same underwater as they do in the air.
Assuming Iron Weights : Conversions factor = 1.16
That is, how much would a hunk of iron have to weigh in the air to weigh what we need underwater.
48 lb X 1.16 = 55.68 lb (56) Persons Wt.
26 lb X 1.16 = 30.16 lb (30) Engine Wt. We Need 96 lb
8.75 lb X 1.16 = 10.15 lb (10) Gear Weight

## Slide 80: Level Flotation Demo
Level FlotationTest with Persons and Gear Weight-
Placement of weights

## Slide 81: Level Flotation Demo
Level Flotation Stability Test with Persons and Gear Weight- Placement of weights

## Slide 82: Level Flotation Demo
Level FlotationTest without Persons Weight-Placement of weights

## Slide 83: FLOTATION
For More information Contact:
US Coast Guard: 202-372-1073
ABYC: 410-990-4450
Me: Spinners110722@yahoo.com